## Slide 1: Logic Design Group 7 Presentation
Jose Escareno III
Logan Gill
Alejandro Henriquez
Brendan Nellis
Jim Yanney

## Slide 2: Problem Statement
Display the Capital letters M, N, O, P and Q using the 17 segment Hex display when the 3 inputs are 0, 1, 2, 3, 4 in order. There will be 3 don’t cares and what is displayed for these does not matter. For the final design use a NOR/NOR two level network.

## Slide 3: Truth Table
A | B | C | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15 | F16
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 0 | 1 | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X
1 | 1 | 0 | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X
1 | 1 | 1 | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X | X
Always on
Always off

## Slide 4: K-Maps
 | A | A’
BC | 0 | 1
BC’ | 0 | X
B’C’ | 1 | X
B’C | 1 | X
F1 & F2 = (A+B) |  | 
 | A | A’
BC | 1 | 1
BC’ | 1 | X
B’C’ | 0 | X
B’C | 1 | X
F4 = (B’+C’) |  | 
 | A | A’
BC | 0 | 1
BC’ | 0 | X
B’C’ | 0 | X
B’C | 1 | X
F5 & F6 = (C’)(A+B) |  | 
 | A | A’
BC | 0 | 0
BC’ | 0 | X
B’C’ | 1 | X
B’C | 0 | X
F9 & F10 = (B)(C) |  | 

## Slide 5: K-Maps
 | A | A’
BC | 1 | 0
BC’ | 0 | X
B’C’ | 0 | X
B’C | 0 | X
F13 = (C’)(B’)(A’) |  | 
 | A | A’
BC | 1 | 0
BC’ | 1 | X
B’C’ | 0 | X
B’C | 0 | X
F14 = (B’)(A’) |  | 
 | A | A’
BC | 0 | 1
BC’ | 1 | X
B’C’ | 0 | X
B’C | 0 | X
F15 = (B’)(A+C) |  | 

## Slide 7: Simplified Logic Expressions (POS)
Always On (1): F3, F7, F8.
Always Off (0): F11, F12, F16.
F1 & F2 = (A+B)
F4 = (B’+C’)
F5 & F6 = (C’)(A+B)
F9 & F10 = (B)(C)
F13 = (C’)(B’)(A’)
F14 = (B’)(A’)
F15 = (B’)(A+C)

## Slide 8: NOR/NOR Implementation
F1 & F2 = ((A + B)’)’
F4 = ((B’ + C’)’)’
F5 & F6 = ((C’)’ + (A + B)’)’
F9 & F10 = ((B)’ + (C)’)’
F13 = ((C’)’ + (B’)’ + (A’)’)’
F14 = ((B’)’ + (A’)’)’
F15 = ((B’)’ + (A + C)’)’

## Slide 10: Shared Terms
((A+B)’)’ for F1, F2, F5, F6
((C’)’)’ for F5, F6, F13
((B)’)’ for F9, F10
((B’)’)’ for F13, F14, F15
((C)’)’ for F9, F10
((A’)’)’ for F13, F14

## Slide 11: Circuit example

## Slide 12: Lessons Learned
A successful engineering team is like any other successful team. It requires shared goals and expectations, effective communication, and respect for each other’s time and abilities.
Logisim is a useful tool that has a slight learning curve.
Modularity and incremental development techniques simplify workflow and enable successively better and better prototypes.